## Slide 1
Matt Haines
matt@electricimp.com

## Slide 2: Slides, Code, etc
https://github.com/beardedinventor/imp201
BlinkUp Credentials
  SSID: impdemo
  PW: electric

## Slide 3: What are we looking at today?
Sleeping
  The sleep methods
  Lazy connections
  The nv table
Building APIs
  The request object
  Simple Security
  Rocky
External Web Services
  http.request API
  Classes, callbacks, and scope

## Slide 4: Pt. 1 - Sleeping

## Slide 5: Agent Code
We’re going to use the following agent code in all of our sleep examples:
/sleeping/sleep.agent.nut

## Slide 6: Sleeping
imp.sleep(timeout)
  Shallow sleeps for timeout seconds
  Code execution continues after the sleep method completes
imp.wakeup(timeout, callback)
  Tells imp to execute callback in timeout seconds.
server.sleepfor(sleepTime)
  Deep sleep (imp disconnects and goes to sleep)
  Imp informs server of deep sleep
imp.deepsleepfor(sleepTime)
  Deep sleep (imp disconnects and goes to sleep)
  Imp doesn't inform server of deep sleep

## Slide 7: imp.sleep
/sleeping/1_impsleep.device.nut

## Slide 8: Why does this stop working?
The imp is single threaded
OS tasks + developer code share the thread
imp.sleep blocks, so the imp can't process messages while we're sleeping
We call readAndSend() inline, so we never actually yield the thread

## Slide 9: imp.wakeup
/sleeping/2_impwakeup.device.nut

## Slide 10: Why is this better?
imp.wakeup is non-blocking
  It tells the imp to schedule some work (the callback) to execute at some time in the future (after the timeout)
imp.wakeup yields the thread (which means OS level tasks, and other messages can be processed)

## Slide 11: server.sleepfor
/sleeping/3_serversleepfor.device.nut

## Slide 12: server.sleepfor
server.sleepfor does two things:
  Puts the imp into a deepsleep for the specified period of time
  Sends a message to the server indicating how long it will be asleep for
[Status] sleeping until 1433784145000

## Slide 13: imp.deepsleepfor
/sleeping/4_impdeepsleepfor.device.nut

## Slide 14: imp.deepsleepfor
imp.deepsleepfor works identically to server.sleepfor, but it doesn't inform the server we're going to sleep
Why do we care?
  Sending messages takes extra power
  Sending messages means we need to connect

## Slide 15: Lazy Connects
On a warm boot*, the imp won't connect until we use a command that requires a connection:
  server.log
  agent.send
  server.sleepfor
  …
* Warm boots are after deep sleeps
* Cold boots are after power cycles

## Slide 16: Lazy Connects
/sleeping/5_lazyconnect.device.nut

## Slide 17: Lazy Connects
After you build and run, it's not going to look like your imp is waking up anymore
LEDs don't blink because it's not connecting
We'll need to push-push (power cycle) in order to force the imp to connect and download new code

## Slide 18: The nv Table
When the imp goes into deepsleep, it looses all state, and begins executing code from the top on wake
The nv table let's us store a small amount of state information/data

## Slide 19: The nv Table
/sleeping/6_nvtable.device.nut

## Slide 20: Pt. 2 – Agent Driven APIs

## Slide 21: Device Code
We’re going to use the following agent code in all of our sleep examples:
/apis/apis.device.nut

## Slide 22: Basic APIs
Getting Started Guide goes through a really simple API example
  Ignores path
  Ignore verb
  No security
  Uses query parameters

## Slide 23: Basic API
/api/1_basicapi.agent.nut

## Slide 24: The request Object
/api/2_request.agent.nut

## Slide 25: Using Paths
Create two paths:
  / returns current state
  /set lets you set state with ?state

## Slide 26: API with Paths
/api/3_paths.agent.nut

## Slide 27: Using Headers for Security
Let's add some security
Requests will need a "X-API-KEY" header
We're going to hardcode the required API-Key

## Slide 28: Using Headers for Security
/api/4_simplesecurity.agent.nut

## Slide 29: Endpoint Specific Security
In the real world, we often need different authentication methods for different end points.
We're going to modify the API so that it only checks for the X-API-KEY when we're trying to set the light

## Slide 30: Endpoint Specific Security
/api/5_endpointsecurity.agent.nut

## Slide 31: This is not maintainable!
We've setup two endpoints, and the code is already a little tricky to follow
A real product might have 5-10+ endpoints with more complicated user access control

## Slide 32: Rocky
https://github.com/electricimp/rocky
#require "Rocky.class.nut:1.1.1"
Allows you to specify behavior by route
Easily add authentication methods to routes
  Easily handle what happens on unauthorized requests
Manage error handling, etc.

## Slide 33: Rocky
/api/6_rocky.agent.nut

## Slide 34: Pt. 3 - Working with web services
We'll be using IFTTT's Maker Channel
(shhhhhh…)
https://ifttt.com/maker

## Slide 35: HTTP Requests
Agents have six APIs to help build requests:
  http.get(url, [headers])
  http.put(url, [headers, body])
  http.post(url, [headers, body])
  http.httpdelete(url, [headers])
  http.request(verb, url, [headers, body]);

## Slide 36: HTTP Requests
/webservices/1_webserviceFunction.agent.nut

## Slide 37: Web Service Classes
Instantiate object with required credentials
All requests should be made asynchronously
Callbacks for requests must take at least two parameters:
  err: null on success, or a string describing the error
  response: The HTTP Response Object
  It's recommended to also require a third parameter:
    data: the decoded data from the request

## Slide 38: Web Service Classes
/webservices/2_webserviceClass.agent.nut

## Slide 39: How to communicate with X Service?
HTTPS
  Inbound data (http.onrequest)
    Service -> Agent -> Device
  Outbound data (http.request)
    Device -> Agent -> Service

## Slide 40: Resources
imp.wakeup https://electricimp.com/docs/api/imp/wakeup
imp.sleep https://electricimp.com/docs/api/imp/sleep
server.sleepfor https://electricimp.com/docs/api/server/sleepfor
imp.deepsleepfor https://electricimp.com/docs/api/imp/deepsleepfor
http.onrequest https://electricimp.com/docs/api/http/onrequest
Rocky https://github.com/electricimp/rocky
http.request https://electricimp.com/docs/api/http/request
Libraries https://electricimp.com/docs/api/examples/libraries

## Slide 41: Questions?